Guidelines

For

Structural Tests and Inspections

For Compliance with the 6th Edition of the

Massachusetts State Building Code

Boston Association Of Structural Engineers

FORMS ONLY

See these Guidelines in their entirety for more information

Chapter 17 Guidelines can be downloaded from

www.b-ase.org

January 1999

3.0	RECOMMENDED FORMS

BASE recommends that SER’s use standard forms when specifying the Program of Structural Tests and Inspections that will be submitted with the application for a building permit, and when writing contracts for services with the owner, other engineering firms, or with testing and inspection agencies.  The following listed forms are recommended by BASE and are included in this section of the Guidelines.

1.	Program of Structural Tests and Inspections.

Instructions.

Forms (to be submitted to the building official with the application for building permit).

2.	Final Report of Structural Tests and Inspections1 (to be submitted by the SER to the building official and to the owner).

3.	Standard Construction Specification Section for Program of Structural Tests and Inspections.

Instructions.

Section 01---:  Structural Tests and Inspections.

4.	Sample Contracts.

Instructions.

Owner - SER Contract (where Owner contracts with Inspection Agencies).

Owner - SER Contract (where SER is responsible for testing and inspection services).

Owner-Inspection Agency Contract.

SER-Inspection Agency Contract.

Program of Structural Tests and Inspections

INSTRUCTIONS

The form Program for Structural Tests and Inspections has two parts: 1) the front two pages which summarize what will be tested and inspected, and who will be doing the tests and inspections; and 2) the pages following the first two, which list the details of the required tests and inspections, with an individual page for each construction category.

Each firm, agency, or individual, who is selected by the Structural Engineer of Record (SER) to perform tests and inspections should be listed as an agent on  page 1, together with an appropriate abbreviation identifying said agent.

The category listing on page 2 encompasses all the construction categories listed in Section 1.1 of these Guidelines.  Check all that apply to the specific program of structural tests and inspections.  Do not check curtain walls unless they have been designed by the SER, or will be designed by other engineers in accordance with a performance specification prepared by the SER.

Following the category listing is a listing of all items which are specified by the SER on a performance basis.  Add items to the listing, as applicable.  Check all that apply.

At the end of the form, list items or systems that are to be excluded from the Program of Structural Tests and Inspections required by the Code.  The exclusions apply when the SER has not been retained to design an item or system or has not been retained to provide a performance specification for an item or system.

The tests and inspections listed under each category of construction have been given in as much detail as is feasible.  The SER should delete all the items that do not apply, add items as he sees fit, and edit the other listed items to suit the project.  The abbreviation for the agent who will be performing the tests or inspections should be given for each item on the final listing.

There are three levels of structural tests and inspections: 1) those specifically mandated in the State Building Code, 2) those which are required by standards referenced by the State Building Code, and 3) those required by the professional judgment of the SER.  All three levels of structural tests and inspections should be included under each category of construction.

The user may find it convenient to develop his own form for the Program of Structural Tests and Inspections, to suit his own practice.  However, the basic features of the BASE form should be included.  Electronic copies of this form are available from BASE.

Boston Association of Structural Engineers

Program of Structural Tests and Inspections

For compliance with the 6th Edition of the Massachusetts State Building Code

Project:	__________________________________________________________________

Location:	__________________________________________________________________

Owner:		__________________________________________________________________

Owner’s Address:	_________________________________________________________

Architect of Record:	_________________________________________________________

Structural Engineer of Record (SER):  ____________________________________________

This program of structural tests and inspections is submitted as a condition for issuance of the building permit in accordance with 780 CMR 1705.0 of the 6th edition of the Massachusetts State Building Code.

The following firms, agencies, or individuals (hereinafter referred to collectively as agents) will perform the tests and inspections under the direction of the SER:

Abbreviation		Agent

SER			Structural Engineer of Record listed above

___________		________________________________________

___________		________________________________________

___________		________________________________________

___________		________________________________________

___________		________________________________________

___________		________________________________________

The abbreviations will be used on the attached pages to identify which agent is performing the particular tests or inspections.

The following categories of structural tests and inspections, if checked, are included in the program for structural tests and inspections for this project. The specific tests and inspections required for each checked category are listed on the page noted opposite the category.

Category

Steel Construction

Cast-in-place concrete
construction

Precast concrete 
construction

Masonry construction

Wood construction

Controlled structural fill (prepared fill)

Page

____

____

____

____

____

____

Category

In-situ bearing strata for
footings

Pile foundations

Pier foundations

Curtain Walls (wall panels
and veneers)

Light gage metal framing

Special cases

Page

_____

_____

_____

_____

_____

_____

The following items of construction, if checked, are specified in the structural plans or specifications on a performance basis.  In accordance with 780 CMR 1705.3.4. their structural design will be reviewed by the SER and their construction is included in the program for tests and inspections on the attached sheets:

Curtain Walls

Precast concrete components

Post-tensioning steel

Structural steel connections

Metal Buildings

________________________________

________________________________

________________________________

The following items are excluded from this program of structural tests and inspections, since they are designed by other structural engineers not under the aegis of the SER and the SER was not retained to provide performance specifications for their design.  These other structural engineers must be assigned by the owner, architect, or construction contractor, as applicable, to be special SER’s for their respective designs and to provide a program of structural tests and inspections for their respective designs.

___________________________________________________________________________

___________________________________________________________________________

Prepared by the Structural Engineer of Record:

Name:_______________________________

Please type or print

Signature:____________________________

Firm:________________________________

Date:________________________________			Registration Seal

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Steel Construction

| Item | Agent | Scope |
| --- | --- | --- |
| Fabricator Certification/ Quality Control Procedures. |
| Review each Fabricator's quality control procedures. |
| Fabricator Inspection. (1705.4.2 and R1705.4.2) |
| Inspect in-plant fabrication, or review Fabricator's approved Independent Inspection Agency's reports. |
| Material Certification. |
| Review for conformance to the specifications. |
| Bolting. |
| Test and inspect bolted connections in accordance with specifications. Verify bolt size and grade. |
| Welding. |
| Check welder qualifications. Visually inspect fillet welds and test full-penetration field welds in accordance with specifications. |
| Shear Connectors. |
| Inspect for size and placement. Test for proper weld attachment. |
| Structural framing, Details and Assemblies. |
| Inspect for size, grade of steel, camber, installation and connection details. Check against approved construction documents and shop drawings. |
| Open Web Steel Joists. |
| Inspect for size, placement, bridging, bearing and connection to structure. Visually inspect all welds of a minimum of 5% of the joists, randomly selected. |
| Metal Decking. |
| Verify gage, width, and type. Inspect placement, laps, welds, sidelap attachment and screws or other mechanical fasteners. Check welder qualifications. |
| Other. |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Cast-in-Place Concrete Construction

| Item | Agent | Scope |
| --- | --- | --- |
| Mix Design. |
| Review mix designs. |
| Materials Certification |
| Review for conformance to specifications. |
| Batching Plant |
| Review Plant quality control procedures and batching and mixing methods. |
| Reinforcement Installation |
| Inspect reinforcing for size, quantity, condition and placement. |
| Post-Tensioning Operations. (1705.6.4) |
| Inspect tensioning and anchorage of tendons. Inspect grouting of bonded tendons. |
| Formwork Geometry |
| Inspect form sizes. |
| Concrete Placement |
| Observe concrete placement operations. Verify conformance to specifications including cold-weather and hot-weather placement procedures. Perform slump, density and air content tests at point of discharge. |
| Evaluation of Concrete Strength |
| Test and evaluate in accordance with the specifications. |
| Curing and Protection |
| Observe procedures for conformance to the specifications. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Precast Concrete Construction

| Item | Agent | Scope |
| --- | --- | --- |
| Plant Certification/Quality Control Procedures. (1705.6.5) |
| Review Plant quality control procedures. Inspect plant storage and handling procedures. Confirm that approved submittals are in the plant and are being used for fabrication. Review welder's certifications. Monitor finished product for structural defects (cracks). |
| Material Certification. (1705.6.1) |
| Review for conformance to ACI 318, Chapter 3. |
| Formwork Geometry. |
| Inspect form sizes. |
| Reinforcement Installation. (1705.6.2) |
| Inspect reinforcing and prestressing strands for size, quantity, condition and placement for conformance with Contract Documents, SER approved submittals, and ACI 318, Sections 7.4, 7.5, 7.6 and 7.7. Inspect welding. |
| Mix Design. (1705.6.3) |
| Review for conformance to ACI 318 and Contract Documents. Inspect for proper mix proportions and mix technique per ACI 318 Chapter 4 and Sections 5.2, 5.3, 5.4 and 5.8. |
| Concrete Placement. (1705.6.3) |
| Inspect concrete placement procedures for conformance to ACI 318, Sections 5.9 and 5.10, and Contract Documents. |
| Curing and Protection. (1705.6.3) |
| Inspect for maintenance of specified curing temperatures and techniques per ACI 318 Sections 5.11, 5.12 and 5.13, and Contract Documents. |
| Evaluation of Concrete Strength. (1705.6.3 and 1908.3.1) |
| Test for conformance to specifications in accordance with ACI 318, Section 5.6, and 780 CMR, Paragraph 1908.3.1. |
| Prestress Operation. (1705.6.4) |
| Inspect application of prestressing forces per ACI 318, Section 18.18. Inspect grouting of bonded, post-tensioned, prestressing tendons. |
| Assembled/Erected Precast Elements. (1705.6.6) |
| Inspect for compliance with SER approved submittals and Contract Documents. Review site storage and handling procedures for consistency with design of precast elements. Verify that SER approved erection drawings are on site and are being used for erection. Verify that SER approved erection procedures are being followed. Observe grouting for all bonded, post-tensioned, pre-stressing tendons. Review welder's certifications. |
| Connections/Embedded Items. |
| Inspect interface connections including end and edge doweling. Inspect embedments for proper location. Inspect shimming, bearing, bolting and welding of connections. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Masonry Construction

| Item | Agent | Scope |
| --- | --- | --- |
| Material Certification |
| Review for conformance to specifications. |
| Evaluation of Masonry Strength |
| Verify strength in accordance with the specifications. |
| Proportioning, Mixing and Consistency of Mortar and Grout |
| Inspect field-mixing procedures for conformance to the specifications. |
| Installation of Masonry |
| Inspect placement for conformance to the specifications. |
| Reinforcement Installation |
| Inspect reinforcing steel for size, quantity, condition and placement for conformance to SER approved submittals and Contract Documents. Inspect welding of reinforcement and review welder's certifications. |
| Grouting Operations |
| Inspect grouting procedures for conformance with the specifications. Inspect cells prior to grouting. |
| Weather Protection |
| Inspect protection for cold and hot weather for conformance with the specifications. |
| Anchorage |
| Inspect anchorage of masonry to other construction for conformance to the Contract Documents. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Wood Construction

| Item | Agent | Scope |
| --- | --- | --- |
| Fabricator Certification/ Quality Control Procedures for prefabricated wood components. |
| Review Fabricator’s quality control procedures. |
| Material Grading. |
| Inspect Lumber for conformance to the Contract Documents. Check moisture content. |
| Framing, Details and Connections. |
| Inspect members for size, placement and connection details. Inspect blocking between floors and at posts. Verify connection hardware and its installation. Inspect bearing, nailing and completed connections for conformance to the SER approved submittals and Contract Documents. |
| Shear Walls and Diaphragms. |
| Inspect thickness and grade of plywood, blocking, hold-down anchors and the edge and field nailing of the plywood to the framing for conformance to the SER approved submittals and Contract Documents. |
| Wood Trusses. |
| Inspect size and location of nail plates, split rings, bolts, or other connection devices for conformance to SER approved submittals and the Contract Documents. Verify that nails, bolts, hold-down anchors or clips or other devices are tight and otherwise properly installed. |
| Laminated Lumber. |
| Inspect nailing, end bearing and end attachment for conformance to SER approved submittals and the Contract Documents. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

In-Situ Bearing Strata for Footings

| Item | Agent | Scope |
| --- | --- | --- |
| Bearing strata for footings |
| Inspect strata for conformance to the structural drawings, specifications, and/or geotechnical report. |
| Bearing surfaces of footings |
| Inspect bearing surfaces for conformance to the requirements of the structural drawings, specifications, and/or geotechnical report. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Controlled Structural Fill (Prepared Fill)

| Item | Agent | Scope |
| --- | --- | --- |
| Fill Material |
| Test material for conformance to specifications or geotechnical report. Perform laboratory compaction tests in accordance with the specifications to determine optimum water content and maximum dry density. |
| Installation of controlled structural fill (780 CMR 1705.9.1 and .2) |
| Provide full-time inspection of the installation, in accordance with the specifications and 780 CMR 1705.9.1 and .2. |
| Density of fill (780 CMR 1705.9.3) |
| Perform field density tests of the in-place fill in accordance with the specifications and 780 CMR 1705.9.3. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Pile Foundations

| Item | Agent | Scope |
| --- | --- | --- |
| Pile material (780 CMR 1816.14) |
| Inspect documents identifying pile material and certifying grade of material for conformance to the Contract Documents, and that the identification is maintained from the point of manufacture to the point of delivery to the site. |
| Pile material tests (780 CMR 1816.14 |
| If Item 1 is unsatisfactory, test material for conformance to the Contract Documents. |
| Precast concrete piles. |
| Perform structural tests and inspections as listed under category Precast Concrete Construction. |
| Pile installation (780 CMR 1816.13) |
| Perform full time inspection of installation. Maintain accurate records for each pile as required in 780 CMR 1816.13. Record final location of each pile in plan. |
| Cast-in-place concrete and reinforcing steel components of piles. |
| Perform structural tests and inspections as listed under category Cast-in-Place Concrete Construction. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Pier Foundations

| Item | Agent | Scope |
| --- | --- | --- |
| Load-bearing steel components. |
| Inspect documents identifying material and certifying grade of material for conformance to the Contract Documents, and that the identification is maintained from the point of manufacture to the point of delivery to the site. |
| Cast-in-place concrete and reinforcing steel components of piles. |
| Perform structural tests and inspections as listed under category Cast-in-Place Concrete Construction. |
| Pier installation (780 CMR 1815.11). |
| Perform full time inspection of installation in accordance with 780 CMR 1815.11. Maintain accurate records for each pier, documenting observations required by 780 CMR 1815.11. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Curtain Walls (Wall Panels and Veneers)

| Item | Agent | Scope |
| --- | --- | --- |
| Precast Concrete Panels. |
| Perform structural tests and inspections as listed under category Precast Concrete Construction. |
| Light Gage Metal Framing for Panels. |
| Perform structural tests and inspections as listed under category Light Gage Metal Framing. |
| Proprietary Light Weight Curtain Walls Systems. |
| Review manufacturer’s fabrication methods and quality control procedures. Review material certification, and inspect fabrication of structural framing, details, connections, and fasteners for conformance to SER approved submittals and the contract documents. |
| Masonry Veneers. |
| Perform structural tests and inspections as listed under category Masonry Construction. Verify that relieving angles, ties to the backup structure, and other structural supports are installed in conformance with the contract documents and SER approved submittals. |
| Aluminum Welding. |
| Review welding procedures and welding qualifications in accordance with AWS D1.2. Observe performance testing of welds required by AWS D1.2. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Light Gauge Metal Framing

| Item | Agent | Scope |
| --- | --- | --- |
| Fabricator’s Quality Control Procedures. |
| Review fabricator’s quality control procedures. |
| Material Certification. |
| Review for conformance to contract documents. |
| Fabrication Inspection. |
| Inspect in-plant fabrication or on-site fabrication. |
| Installation. |
| Verify that type, size, quantity, location, details, and connections of framing members conform to SER approved submittals, and the contract documents.. |
| Welding. |
| Check welders’ qualifications. Verify that welding conforms to AWS specifications, SER approved submittals, and the contract documents. Visually inspect welds. |
| Other Fasteners. |
| Verify fastener type and installation procedures. Verify that fasteners conform to SER approved submittals and the contract documents. Verify that fasteners are installed tight. |
| Other |

Schedule of Structural Tests and Inspections		Page _____ of _____

Project: _________________________

Special Cases

| Item | Agent | Scope |
| --- | --- | --- |

Boston Association of Structural Engineers

Final Report of Structural Tests and Inspections

For compliance with the 6th Edition of the Massachusetts State Building Code

| Project: |
| --- |
|  | Location: |
|  | Owner: |
|  | Owner's Address: |
| Architect of Record: |
|  | Structural Engineer of Record: |

To the best of my information, knowledge and belief, the structural tests and inspections itemized in the Program of Structural Tests and Inspections submitted for permit have been satisfactorily completed and all discovered defects have been corrected.

Comments:

The Program of Structural Tests and Inspections does not relieve the Contractor or its subcontractors of their responsibilities and obligations for quality control of the work, for any design work which is included in their scope of services, and for full compliance with the requirements of the Construction Documents.  Furthermore, the detection of, or the failure to detect, deficiencies or defects in the work during testing and inspection conducted pursuant to the Program does not relieve the Contractor or its subcontractors of their responsibility to correct all deficiencies or defects, whether detected or undetected, in all parts of the work, and to otherwise comply with all requirements of the Construction Documents.

| Respectfully Submitted, Structural Engineer of Record |
| --- |
| Type or print name |
|  | Signature | Date |
| Registration Seal |

Standard Construction Specification Section for

Program of Structural Tests and Inspections

INSTRUCTIONS

This specification section should be inserted into Division 1 of the project specifications. When an architect is the prime professional, the SER should give the architect a copy of this section and request that it be included in the project specifications. The criteria of this section protects the owner, the architect, and the structural engineer.

Alternatively, this section can be included as an article in the general or supplementary general conditions.

The terms Contract Documents and Work are as defined in AIA Document 201, General Conditions of the Contract for Construction. If other terms are used in lieu of these terms in the contract, conditions of the contract, or specifications, they should be defined in an appropriate contract document.

Paragraph 1.02.A covers the situation where 780 CMR 1705 requires structural tests and inspections for a component or a system, for which the SER has provided neither a structural design nor a performance specification. If this situation does not apply to the project, then this paragraph should be deleted.

SECTION 01---
STRUCTURAL TESTS AND INSPECTIONS

1.01	General

A.	The 6th Edition of the Massachusetts State Building Code, 780 CMR, under which this project is designed and will be built, requires the structural engineer of record (SER) to provide a program of structural tests and inspections for this project in accordance with 780 CMR 1705. The SER is the structural engineer (an individual) who is in responsible charge of the preparation of the structural drawings and structural specifications for this project and whose Massachusetts professional engineering seal appears on said structural drawings.

B.	The SER has prepared a document entitled Program of Structural Tests and Inspections, which has been or will be submitted to the building official who has jurisdiction over this project, with the application for a building permit.

C.	The program of structural tests and inspections shall not relieve the Contractor or its subcontractors of their responsibilities and obligations for quality control of the Work, their other obligations for supervising the work, for any design work which is included in their scope of services, and for full compliance with the requirements of the Contract Documents. Furthermore, the detection of, or failure to detect, deficiencies or defects in the Work during the testing and inspection conducted pursuant to the program shall not relieve the Contractor or its subcontractors of their responsibility to correct all deficiencies or defects, whether detected or undetected, in all parts of the Work, and to otherwise comply with all requirements of the Contract Documents.

D.	The program of structural tests and inspection does not apply to the Contractor’s equipment, temporary structures used by the Contractor to construct the project, the Contractor’s means, methods, and procedures, and job site safety.

1.02	CONTRACTOR’S RESPONSIBILITIES

A.	Where the document Program of Structural Tests and Inspections indicates that a structural component or system is subject to structural tests and inspections by 780 CMR 1705 and that the SER for the project has not been retained to design said component or system or to prepare a performance specification for said component or system, and the Architect has not otherwise provided for the structural design of said component or system, the Contractor shall retain, or require others under his aegis to retain, a professional engineer registered in Massachusetts to design said component or system and to provide the required program of structural tests and inspections for said component or system.

B.	The Contractor shall provide free and safe access to the Work for the SER and all other individuals who are observing the Work or performing structural tests or inspections. The Contractor shall provide all ladders, scaffolding, staging, and up-to-date safety equipment, all in good and safe working order, and qualified personnel to handle and erect them, as may be required for safe access.

C.	The Contractor shall give reasonable notice to the SER, or to those performing inspections and tests under the SER’s direction, of when the various parts of the Work will be ready for inspection. The Contractor shall obtain instructions from the SER as to what is reasonable notice for the various aspects of the work, and who is to be notified.

D.	The Owner reserves the right to back charge the Contractor for additional expense incurred by the Owner for the services of the SER or those under his direction when work is not reasonably ready for inspection in accordance with the notice provided by the Contractor.

Sample Contracts

INSTRUCTIONS

1.	There are four sample contracts which follow these instructions and to which these instructions apply. The contracts are designed to be used in pairs, as follows:

When the owner directly hires the outside inspection agencies selected by the SER:

A.	Owner - Structural Engineer of Record Contract (where Owner contracts with Inspection Agencies)

B.	Owner - Inspection Agency Contract

When the SER selects and retains the outside inspection agencies:

C.	Owner - Structural Engineer of Record Contract (where the SER is responsible for testing and inspection services)

D.	Structural Engineer of Record - Inspection Agency Contract

2.	For the purposes of these contracts (only), the Structural Engineer of Record (SER) is the firm (single proprietorship, partnership, or corporation) which employs the individual structural engineer whose professional engineering seal appears on the structural design documents submitted with the building permit application. For the purposes of 780 CMR 1705.0, the SER is the said individual structural engineer.

3.	The structural engineering firm should review the sample contracts with its attorney and insurance advisor, and adapt the sample contracts to the needs of the firm and the particular project. The structural engineering firm should insure that there is no conflict between the firm’s contract with the architect for structural design services and the contract with the owner for structural tests and inspections.

4.	Contracts with inspection agencies: The SER should develop a detailed scope of structural testing and inspection services that will be performed by each particular inspection agency, and specify same in Exhibit A of that agency’s contract. The SER should also negotiate the rates for payment with that inspection agency and specify them in Exhibit B. Where the owner hires the inspection agencies directly, the SER (the firm) will be acting as the owner’s agent in these regards.

5.	Indemnity: The contracts with the inspection agencies require that the inspection agency indemnify the SER, owner, and architect for the inspection agency’s negligence. The purpose of this indemnity is to provide an equitable distribution of risk considering that the SER has less control over the actions of the inspection agencies than the actions of its own personnel. These indemnities must be backed-up with adequate insurance; the recommended minimum coverage and other requirements are given in the contracts. The indemnity provisions exclude defense costs since professional liability insurance does not include coverage for defense costs.

Most owner-architect, owner-engineer, or architect-engineer design contracts do not include provisions for indemnification of the owner (e.g. AIA B141 and EJCDC 1910-1), since most architects and engineers do not consider providing indemnification of the owner to be equitable. The Owner-SER contracts herein also do not include indemnification of the owner for the same reason. However, some owners may request indemnification from the SER firm. If this is agreeable to the SER firm, the firm should make sure that the requested indemnification is negligence based and does not include defense costs. Further, the firm should consult with its attorney and obtain approval of the indemnification clause from its insurance carrier.

OWNER-STRUCTURAL ENGINEER OF RECORD CONTRACT

(where Owner contracts with Inspection Agencies)

The following constitutes the terms of the Agreement between __________________________________ (“Owner”) and _________________________ (“Structural Engineer of Record” or “SER”) with respect to the performance of its services for the ________________________(“the Project”).

1.	SCOPE OF SERVICES

The SER shall establish and direct a program of structural tests and inspections in accordance with the Massachusetts State Building Code, 780 CMR 1705.0.

As required by 780 CMR 1705.3, the SER shall select all personnel who will perform structural tests and inspections.  Said personnel may be from the SER’s firm, other engineering firms, individuals, inspection agencies, or testing firms.  The SER shall direct and coordinate the activities of said personnel.

As required by 780 CMR 1705.3.4, the SER shall review the following designs for which it provided a performance specification and for which said review is not included in the scope of services of the architect-structural engineer contract for this project: ________________________________________________________  ___________________________________________________________________________________________

For testing and inspection services which will not be performed by the SER’s firm, the SER shall, as an agent of the Owner, assist in the negotiation of agreements between the Owner and the inspection agencies selected by the SER.  The inspection agencies shall be solely responsible for the performance of its structural testing and inspection services, and the SER shall be entitled to rely upon such performance.  Nothing herein shall be construed so as to establish a contractual relationship between the SER and the inspection agencies.

The SER shall, as an agent of the Owner, review invoices submitted by the inspection agencies in connection with the performance of the testing and inspection services.  In connection with such review, the SER will either approve an invoice for payment or return it to the inspection agency for further information. The SER shall not, however, be responsible for the payment of such invoices.

2.	INDEMNIFICATION

The Owner shall require the inspection agencies to indemnify and hold harmless the SER and the Architect from and against all claims, costs and liability arising out of or resulting from the performance of the testing and inspection services.

3.	INSURANCE

The Owner shall require that the inspection agencies obtain at their own expense, to have in force before commencing any services, and for a six-year period beyond the date of substantial completion of the project, the following insurance:

A.	Comprehensive General Liability Insurance providing for a combined single limit of One Million Dollars ($1,000,000.00) for bodily injury, death and property damage; and

B.	Professional Liability Insurance with a limit of One Million Dollars ($1,000,000.00) per claim and in the aggregate.

Insurance certificates evidencing the above coverage shall be issued to the Owner and the SER prior to commencement of the testing and inspection services and shall specify that the Owner and the SER must be given, in writing, thirty (30) days notice of cancellation, termination, or alteration of the policies evidenced by the certificate.

4.	LIMITATIONS TO SERVICES

Structural tests and inspections are for quality assurance audits and their implementation is not intended to relieve the construction contractor or its subcontractors of their responsibility for quality control of the work and for any design for which they are responsible.  The Owner shall include a statement to this effect in the construction contract.

5.	TERMS OF PAYMENT

The Owner shall pay the SER for the scope of services set forth herein, in accordance with the rates listed in Exhibit A attached hereto, based upon invoices submitted by the SER.

The period covered by each invoice shall be one calendar month ending on the last day of the month.

The Owner shall review all invoices within seven days of receipt.  If said invoices are appropriate, the Owner shall pay the invoiced amount within ___ days of receipt; if the invoices are not appropriate, he shall send them back to the SER for correction.

EXECUTED:

As of this ____ day of ________, 19___.

OWNER:

STRUCTURAL ENGINEER OF RECORD:

OWNER-STRUCTURAL ENGINEER OF RECORD CONTRACT

(where SER is responsible for testing and inspection services)

The following constitutes the terms of the Agreement between __________________________________ (“Owner”) and ________________________ (“Structural Engineer of Record” or “SER”) with respect to the performance of its services for the ________________________(“the Project”).

1.	SCOPE OF SERVICES

The SER shall provide and be responsible for the performance of the structural tests and inspections as required by 780 CMR 1705.0.

As required by 780 CMR 1705.3.4, the SER shall review the following designs for which it provided a performance specification and for which said review is not included in the scope of services of the architect-structural engineer contract for this project: ________________________________________________________

___________________________________________________________________________________________

2.	LIMITATIONS TO SERVICES

Structural tests and inspections are for quality assurance audits and their implementation is not intended to relieve the construction contractor or its subcontractors of their responsibility for quality control of the work and for any design for which they are responsible.  The Owner shall include a statement to this effect in the construction contract.

3.	TERMS OF PAYMENT

The Owner shall pay the SER for the scope of services set forth herein in accordance with the rates listed in Exhibit A attached hereto, based upon invoices submitted by the SER.

The period covered by each invoice shall be one calendar month ending on the last day of the month.

The Owner shall review all invoices within seven days of receipt.  If said invoices are appropriate, the Owner shall pay the invoiced amount within ___ days of receipt; if the invoices are not appropriate, he shall send them back to the SER for correction.

EXECUTED:

As of this ____ day of ________, 19___.

OWNER:

STRUCTURAL ENGINEER OF RECORD:

OWNER-INSPECTION AGENCY CONTRACT

The following constitutes the terms of the Agreement between _______________________________

(“Owner”) and _________________________ (“Inspection Agency” or “the Agency”) with respect to the performance of its services for the ____________________(“the Project”).

1.	SCOPE OF SERVICES

The Agency shall perform the Structural Testing & Inspection Services listed in Exhibit A attached hereto, as directed by the Structural Engineer of Record (“SER”).

It is understood and agreed that in the performance of the Structural Testing & Inspection Services required by this Agreement, the Agency is acting in the capacity of an independent contractor, as currently defined at law, and that the relationship of employer and employee shall not exist between the Owner and the Agency.

2.	RELIANCE ON SERVICES AND RESPONSIBILITY FOR DATA

It is understood and agreed that the Owner and the SER shall be entitled to rely upon, and the Agency shall be fully responsible for, the accuracy and completeness of the Agency’s performance of the services, including any data, test results, evaluative material, tests, reports or studies developed or prepared by the Agency.

3.	QUALIFICATIONS OF PERSONNEL

The Agency shall provide personnel who are qualified by education, training, and experience to perform the testing and inspection services listed in Exhibit A.  The Agency shall submit the qualifications of said personnel to the SER for the SER’s approval.  Only personnel approved by the SER may be used.  Where a statute or the State Building Code requires a license or certification for a particular task, all personnel performing said tasks shall be so licensed or certified.

4.	INDEMNIFICATION

The Agency hereby agrees to indemnity and hold harmless the Owner, SER, and Architect from and against all claims, costs and liability arising out of the Agency’s services hereunder, to the extent that such claims, costs and liability are the result of negligent acts, errors or omissions of the Agency, or breach by the Agency of its obligations hereunder.

5.	INSURANCE

The Agency agrees to obtain at its own expense, and to have in force before commencing any services, and for a six-year period beyond the date of substantial completion of the project, the following insurance:

A.	Comprehensive General Liability Insurance providing for a combined single limit of One Million Dollars ($1,000,000.00) for bodily injury, death and property damage; and

B.	Professional Liability Insurance with a limit of One Million Dollars ($1,000,000.00) per claim and in the aggregate.

All insurance coverage shall be through a company or companies acceptable to the Owner. Insurance certificates evidencing the above coverage shall be issued to the Owner and the SER prior to commencement of the Structural Testing & Inspection Services and shall specify that the Owner  and the SER must be given, in writing, thirty (30) days notice of cancellation, termination, or alteration of the policies evidenced by the certificate.

6.	LIMITATIONS TO SERVICES

Structural tests and inspections are for quality assurance audits and their implementation is not intended to relieve the construction contractor or its subcontractors of their responsibility for quality control of the work and of any design for which they are responsible.  The owner shall include a statement to this effect in the construction contract.

7.	TERMS OF PAYMENT

The Owner shall pay the Agency for the testing and inspection services listed in Exhibit A, in accordance with the rates listed in Exhibit B attached hereto, based upon invoices submitted to and approved by the SER.

The period covered by each invoice shall be one calendar month ending on the last day of the month.

The SER shall review the invoices submitted by the Agency within seven days of receipt.  If said invoices are appropriate, the SER shall approve and forward the invoices to the Owner for payment; if the invoices are not appropriate, the SER shall send them back to the Agency for correction.

Invoices approved by the SER shall be paid by the Owner within ___ days of receipt by the SER.

EXECUTED:

As of this ____ day of ________, 19___.

OWNER:

INSPECTION AGENCY:

STRUCTURAL ENGINEER OF RECORD-
INSPECTION AGENCY CONTRACT

The following constitutes the terms of the Agreement between _______________________________ (“Structural Engineer of Record” or “SER”) and _________________________ (“Inspection Agency” or “the Agency”) with respect to the performance of its services for the ________________________(“the Project”).

1.	SCOPE OF SERVICES

The Agency shall perform the Structural Testing & Inspection Services listed in Exhibit A attached hereto, as directed by the Structural Engineer of Record (“SER”).

It is understood and agreed that in the performance of the Structural Testing & Inspection Services required by this Agreement, the Agency is acting in the capacity of an independent contractor, as currently defined at law, and that the relationship of employer and employee shall not exist between the SER and the Agency.

2.	RELIANCE ON SERVICES AND RESPONSIBILITY FOR DATA

It is understood and agreed that the SER, Owner and Architect shall be entitled to rely upon, and the Agency shall be fully responsible for, the accuracy and completeness of the Agency’s performance of the services, including any data, test results, evaluative material, tests, reports or studies developed or prepared by the Agency.

3.	QUALIFICATIONS OF PERSONNEL

The Agency shall provide personnel who are qualified by education, training, and experience to perform the testing and inspection services listed in Exhibit A.  The Agency shall submit the qualifications of said personnel to the SER for the SER’s approval.  Only personnel approved by the SER may be used.  Where a statute or the State Building Code requires a license or certification for a particular task, all personnel performing said tasks shall be so licensed or certified.

4.	INDEMNIFICATION

The Agency hereby agrees to indemnity and hold harmless the SER, Owner and Architect from and against all claims, costs and liability arising out of the Agency’s services hereunder, to the extent that such claims, costs and liability are the result of negligent acts, errors or omissions of the Agency, or breach by the Agency of its obligations hereunder.

5.	INSURANCE

The Agency agrees to obtain at its own expense, to have in force before commencing any services, and for a six-year period beyond the date of substantial completion of the project, the following insurance:

A.	Comprehensive General Liability Insurance providing for a combined single limit of One Million Dollars ($1,000,000.00) for bodily injury, death and property damage; and

B.	Professional Liability Insurance with a limit of One Million Dollars ($1,000,000.00) per claim and in the aggregate.

All insurance coverage shall be through a company or companies acceptable to the SER.  Insurance certificates evidencing the above coverage shall be issued to the SER prior to commencement of the Structural Testing & Inspection Services and shall specify that the SER must be given, in writing, thirty (30) days notice of cancellation, termination, or alteration of the policies evidenced by the certificate.

6.	TERMS OF PAYMENT

The SER shall pay the Agency for the testing and inspection services listed in Exhibit A, in accordance with the rates listed in Exhibit B attached hereto, based upon invoices submitted by the Agency to the SER and as set forth herein.

The period covered by each invoice shall be one calendar month ending on the last day of the month.

The SER shall review the invoices submitted by the Agency within seven days of receipt.  If said invoices are appropriate, the SER shall approve and forward the invoices to the Owner for payment.  The SER shall pay the invoices within ___ day of receipt of payment by the Owner.  If the invoices are not appropriate, the SER shall send them back to the Agency for correction.

EXECUTED:

As of this ____ day of ________, 19___.

STRUCTURAL ENGINEER OF RECORD:

INSPECTION AGENCY:

# Footnotes

Portions of these forms are adapted with permission from Connecticut Engineers in Private Practice, Structural Engineers Coalition, Form 101 - Statement of Special Inspections, Copyright 1993.